## Slide 1: A universal two-qubit computational register for trapped-ion quantum processors
1Institut für Quantenoptik, Leibniz Universität Hannover, Welfengarten 1, 30167 Hannover
2PTB, Bundesallee 100, 38116 Braunschweig
3QUDORA Technologies GmbH, Wilhelmsgarten 3, 38100 Braunschweig
Nicolas Pulido-Mateo1,2, Hardik Mendpara1,2, Markus Duwe1,2, Giorgio Zarantonello1,3, Amado Bautista-Salvador1,2,3, Ludwig Krinner1,2 and Christian Ospelkaus1,2,3
Notes: Transition 1
Hello, my name is Nicolas Pulido and the title of my talk is "A universal two-qubit computational register for trapped –ion quantum processors".
I'm a PhD student in Chrisitan Ospelkaus' group and I'm officially from the Institute of Quantum Optics in Hannover but my lab is at PTB Braunschweig.
I'm going to talk about how we built a two-qubit register that can act as the computational core in a quantum processor based in trapped ions

## Slide 2: Motivation
QVLS-Q1
  Trapped-ion based
  QCCD architecture
  Surface-electrode trap
  Multizone:
    Trapping
    Storage
    State preparation and readout
    Computation
Characterization and benchmarking
  Universal set of gates
    Two-qubit entangling gate
    Single-qubit rotations
D. Wineland et al., J. Res. NIST 103 (1998)
D. Kielpinski et al., Nature 417 (2002)
https://www.qvls-q1.de

## Slide 3: Outline
Experimental setup
Two-qubit entangling gates
Single-qubit rotations
Cycle Benchmarking experiment
Discussion
Notes: Add part of greater project QCLS Q1

## Slide 4: Beryllium: State preparation
Microwave hop to |0⟩
State initialization in |2,2⟩
Physical sequence:
Doppler cooling
Microwave hop to |1⟩
Ground-state cooling
Notes: No more thatn 30 seconds, just read bullets

## Slide 5: Microwave near-field
d
+
I ()
Transition | Speed | Scaling
Carrier |  | 
Sidebands |  | 
2nd Sidebands |  | 
3rd Sidebands |  | 
Transition | Speed | Scaling
Carrier |  | 
Sidebands |  | 
2nd Sidebands |  | 
3rd Sidebands |  | 
Microwave conductor
I ()
+
+
Impact of residual B-field:
  AC Zeeman shift (gate-error)
Notes: In the MW n.f. approach ion is located close to conductor at a distance d ...
Figure
From theory of interaction between.. Table
In the near-field d<< where the B’ amplitude goes as...
Sidebands necessary for multi-qub gates since they couple..
The presence of Bres field can lead to problems such as..
To avoid the issue, is possible to use multiple conduct.. figure
In the MW n.f. approach ion is located close to conductor at a distance d ...
Figure
From theory of interaction between.. Table
In the near-field d<<𝜆 where the B’ amplitude goes as...
Sidebands necessary for multi-qub gates since they couple..
The presence of Bres field can lead to problems such as..
To avoid the issue, is possible to use multiple conduct.. figure

## Slide 6: Microwave near-field engineering
Embedded single microwave conductor in surface-electrode ion trap
Single conductor intrinsically phase and amplitude stable
Geometry can be optimized to suppress residual field
+
d
MWM
excitation
M. Carsjens et al., Appl. Phys. B 114, 423-250 (2014)
Notes: In our system we use single MW cond with 3 segments.
Which ensures relative phase and amp stabil
The conductor generates B field quadrupole with strong B’ and supress B
The cond is integrated in our SE ion trap.
Where the ion is confined with ....
Since we use a single conductor the B field properties are fixed by geomtry
To predict generated field we need to simulate it
We use commercial software to do FEM sim which accounts for many effects such as..
From result we can extract useufl info, currents and B

## Slide 7: Mølmer-Sørensen gate
Klaus Mølmer and Anders Sørensen Phys. Rev. Lett. 82 (1999)

## Slide 8: Mølmer-Sørensen gate: Fidelity analysis
Effect | Infidelity
Mode instability | 1.3 × 10-2
Spectator mode | 5.2 × 10-3
Motional heating | 3.8 × 10-3
scan φ
Hahn et al., npj Quantum Inf 5, 70 (2019)
Sackett et al., Nature 404, (2000)

## Slide 9: Mølmer-Sørensen gate: Pulse shaping
Zarantonello et al., PRL, 123, (2019)
M Duwe et al 2022 Quantum Sci. Technol. 7 045005

## Slide 10: Single-ion addressing
x
Qubit 2
Qubit 1
Trap center
+
+
Rotate ion crystal
Displace ion to be addressed out of micromotion minimum
Micromotion sideband interaction
U. Warring et al., PRL 110, 173002 (2013)
D. Leibfried –PRA 60, R3335(R), (1999)

## Slide 11: Single-ion addressing: Flopping and crosstalk
Ωion0 = 2π × 11.145(5) kHz
Ωion1 = 2π × 5.655(5) kHz
scan t
Piltz et al., Nat Commun 5, 4679 (2014)

## Slide 12: Simple circuits: Cycle benchmarking
Erhard et al., Nat Commun 10, 5347 (2019)
repeat mj times

## Slide 13: Discussion
Why 96.6 % fidelity?
Calibration errors
  Mode​ / detuning
    We are robust
  AC Zeeman shift
    Need order of magnitude more
  Phase (principal suspect)
    Offset between 1 and 2-qubit gates
    Frame of reference
    10o per circuit?

## Slide 14: Acknowledgments
Thanks to my colleagues:
  Hardik Mendpara, Markus Duwe, Christian Joohs a.k.a. CJ, Alexander Onkes, Yannick Hermann, Giorgio Zarantonello, Amado Bautista-Salvador, Ludwig Krinner, Christian Ospelkaus, …
Thanks to the Alumni:
  M. Wahnschaffe, H. Hahn, …
We greatly acknowledge all of our third-party funding